## Slide 1
August 2000
SiS VGA Product Roadmap
SiS315 Presentation
Lightning Speed, Beyond Fantasy

## Slide 2
Agenda
SiS315 Positioning / Strategy
GPU Block Diagram
Feature Introduction
Performance Comparision

## Slide 3
SiS315 Positioning
Mainstream Marketing
    SiS315 => 128 bit SDR/ 64-bit SDR
    Focus on 32M
    Best Cost / Performance
    Support Cost-Effective Memory Configuration

## Slide 4
SiS315 Market Strategy
The Best Choise for Sub-U$90 3D VGA Solution
  The Perfect Choise with 3DVR
  The Best 3D Performance you Can Get
  The Richest Multimedia Function You Can See
  The Flexible Display Option You Can Select

## Slide 5
SiS315 Block Diagram
AGP2X/4X
Address
Data
1’st Monitor
100 Pin TQFP
SiS301
LCD Monitor
TV
2’nd Monitor
64/128 SD/SGRAM Interface
64/128 DDR Interface
DRAM
2nd Transform & Lighting
New Gen. 256 Bit 3D Engine
3D VR inside
Visibility Engine
Hyper FSAA
529 BGA

## Slide 6
256-bit Graphics Architecture
Transform And Lighting 3D Engine
DirectX 7.x/OpenGL ICD
SDRAM/SGRAM /DDR DRAM Interface
166MHz Memory Clock
Integrated 3D VR Eyeglass Circuit
Motion compensation
Maximum 128 MB Local Frame Buffer
375 MHz RAMDAC
0.15um CMOS Technology
529 balls BGA package
Utilized With SiS301 To Support Dual Display Solution
    VGA + 2nd VGA
    VGA + TV (NTSC / PAL)
    VGA + LCD Monitor (TMDS),Up To 1280x1024
Key Feature

## Slide 7
Secondary CRT_Out
  Independent Resolution,Color Depth & Frame Rate
  Secondary DDC interface
  135 MHz 2’nd RAMDAC Up To 1280x1024@85Hz
LCD Monitor_Out
  Integrated TMDS Transmitter
  DVI Compliant
  Support 18” LCD Up To 1280 * 1024 Resolution
  Hot Plugging Function Defined By VESA P&D 1.0
NTSC/PAL TV_Out
  Programmable 6 Line Buffers Anti Flickering Filter
  Macro Vision Ver. 7.1.L1
The SiS301 for SiS315

## Slide 8
Test Environment:
GIGABYTE (Intel 815)
Pentium !!! 1GHz MHz,128MB
Windows 98SE
SiS315 /32M
ECLK/MCLK=166/166MHz
Driver version:v2.01.04
MX200 /32M
ECLK/MCLK=175/166MHz
Driver version: v0650(get from offical web-site)
3DMARK 2001 V1.1
(1024 x 768 x 32bpp @ 85Hz )
Performance Leading
3D MARK2000 pro V1.1
(1024 x 768 x 32bpp @ 85Hz)

## Slide 9
Test Environment:
GIGABYTE GA-60XM7E (Intel 815)
Pentium !!! 1G MHz,128MB
Windows 98SE
Gaming Benchmark
Direct 3D
Unreal Tournament (1024X768X32)
OpenGL
SiS315 /32M
ECLK/MCLK=166/166MHz
Driver version:v2.01.04
MX200 /32M
ECLK/MCLK=175/166MHz
Driver version: v0650(get from offical web-site)
MDK2 (1024X768X32)